## Slide 1: The Internet in Transition: The State of IPv6 in Today’s Internet
Geoff Huston
Asia Pacific Network Information Centre

## Slide 2: The Internet...
has been a runaway success that has transformed not just the telecommunications sector, but entire commercial and social systems are being transformed by the Internet
Time
Almost Anything
Internet

## Slide 3: Growth Pressures
The protocol was designed in an era of mainframe computers, where the largest networks of the day connected 100’s of devices
The same protocol is being used today in a context of use that spans billions of devices
We confidently anticipate further growth

## Slide 4: Scaling Critical Infrastructure
Silicon-based equipment scales with Moore’s Law
  As long as the aggregate growth rate is below doubling every two years economies of scale still hold in this area
Names scale within the structure of a loose hierarchy
  Adding name names at the leaf points of the name structure scales at a level of O(n)
Addresses are fixed size elements in the protocol
  And this is a problem, and has been recognised as a problem for more than 20 years
  It’s now an urgent issue because of the exhaustion of IPv4 addresses in AsiaPac, Europe and the Middle East

## Slide 6: Extending IP Addresses
New protocol header
lengthen the address field by adding more bits to the packet header
Preserves the architecture of the network
Issues about backward compatibility
“Share” an address across multiple users
Use the transport protocol bits to share a single address
Preserves the application functionality of the network
Backward compatible
Destroys the architecture of the network
IPv6
NATs

## Slide 7: IPv6
Protocol defined in the mid-90’s
Reference open source implementations available mid-late 90’s
Now implemented for most device platforms and enabled for use (Microsoft Windows, Apple OSX and iOS, Android, Linux, ...)

## Slide 8: Deploying IPv6
All devices need to be reprogrammed to include an IPv6 stack in addition to an IPv4
Infrastructure elements need to be re-configured to include IPv6 access as well as IPv4
Access networks and CPE need to be re-configured/replaced to support IPv6 as well as IPv4

## Slide 9: Deploying IPv6
All devices need to be reprogrammed to include an IPv6 stack in addition to an IPv4
Infrastructure elements need to be re-configured to include IPv6 access as well as IPv4
Access networks and CPE need to be re-configured/replaced to support Ipv6 as well as IPv4
Well underway – more than 50% of devices now support IPv6
Underway - transit services, DNS services, content services being reconfigured
This is a potential problem area!

## Slide 10: IPv6 capability, as seen by Google
Source: http://www.google.com/intl/en/ipv6/statistics/
In November2012 only 0.9% of users access to Google’s dual stack
services used IPv6

## Slide 11: IPv6 capability, as seen by APNIC
Source: http://labs.apnic.net/ipv6-measurement/Regions/001%20World/
% of Users

## Slide 12: Where is it?
http://labs.apnic.net/index.shtml
% of users preferring IPv6 – per country

## Slide 13: Why is IPv6 not happening?
The major issue appears to be in the business structure of the “last mile” access networks
The usual business incentives that would drive investment in new services appear to be lacking for IPv6 – IPv6 represents cost without benefit for many access providers

## Slide 14: What happened 20 years ago?
If IPv6 is such a problem today then how did this industry adopt IPv4 in the first place?

## Slide 15: PSTN Circuits to IP Packets: The Demand Schedule Shift
Quantity
Price
q(Circuits)
q(IP)
p(IP)
p(Circuits)
reduced cost of
supply, and increased
perception of value,
resulting in a new
equilibrium point with
higher quantity and
lower unit price
s(IP)
s(C)
d(IP)
d(C)

## Slide 16: IPv6 vs IPv4
Are there competitive differentiators?
cost4 = cost6
functionality4 = functionality6
no inherent consumer-visible difference
no visible consumer demand
no visible competitive differentiators other than future risk

## Slide 17: IPv4 to Dual Stack: The Demand Schedule Shift
Quantity
Price
QV4
PV4
SV4
SDualStack
DV4 / DualStack
PDualStack
QDualStack
Supply side cost increase due to Dual Stack operation
No change in perception of value, so demand schedule is unaltered
Equilibrium point is at a lower quantity if Dual Stack supply costs are passed on to customers

## Slide 18: The Transition to IPv6
Given that
  we’ve left it so late in terms of the scale of the transition
  the degree of difficultly with IPv4 exhaustion
  there appears to be little economic motivation from the carriage side of the industry to embark on this transition
Will market forces actually drive the industry to adopt IPv6 at all?

## Slide 19: The Alternative to IP6
Increase the density of NATs by adding CGNs to the carriage infrastructure
CGNs share a single address across multiple customers by multiplexing on the transport port addresses
This can be achieved incrementally, with modest outlay, and without altering the customer’s equipment or applications, and without coordination with any other provider or content delivery system
With IPv4 exhaustion this is a forced decision – once a SP runs out of IPv4 addresses this is a cost effective option to support further growth

## Slide 20: IPv4 to CGNs: The Demand Schedule Shift
Quantity
Price
QV4
PV4
SV4
SCGN
DV4 / DualStack
PCGN
QCGN
Supply side cost decrease due to CGN operation offset by opportunities for leverage
over content
No change in perception of value, so demand schedule is unaltered
Based on leverage over content CGNs may produce a preferred outcome for the access provider market

## Slide 21: Carriage vs Content
The architecture of the Internet struck a new balance between carriage and content:
  Content no longer required the permission of the carriage providers
  Any form of content, delivered in any fashion that optimized the efficiency of the user’s interaction with the content could be implemented on the Internet
  The carriage network was unaware of the nature of the content and service transactions
The value of the “Internet Economy” is the value of this redefinition of the provision of goods and services, and the removal of carriage level impositions and overheads from the picture

## Slide 22: Carriage vs Content
Carrier NATs in IPv4 fundamentally change this balance:
  Carriage providers have direct visibility of all user transactions
  Carriers can directly alter the quality of the service delivered to users for individual services through manipulation of CGN behavior
  Carriers can directly create barriers of access to users, forcing content providers to pay an access premium for direct access to the carrier’s user base
  There is no efficient alternative for content to access users given the address exhaustion issue and the unique local monopoly position of access providers

## Slide 23: CGN Risks
The CGN approach was intended to be a stopgap measure for IPv4 address exhaustion
But there are long term risks here:
  The major risk is that the incumbent content providers join with the incumbent carriers to exploit this situation to create:
    elevated barriers to entry for new content
    limitations on the forms of innovation for content delivery
  Incumbents in carriage and content are then in a unique position to define the terms and conditions for future competition
    This may result in a small number of actors with overarching control of carriage and content over the entire communications system

## Slide 24: Why IPv6?
IPv6 represents the most efficient path to support an open network that can sustain efficient competitive access to the carriage and content service roles
And efficient competitive access to all parts of this activity underpin almost all of the expectations of future efficient growth of the Internet Economy

## Slide 25: The 2008 Seoul Declaration for the Future of the Internet Economy
"Encourage the adoption of the new version of the Internet protocol (IPv6), in particular through its timely adoption by governments as well as large private sector users of IPv4 addresses, in view of the ongoing IPv4 depletion."